## Slide 1: ECE808: Smart Water Systems using the EPANET-MATLAB Toolkit
Demetrios ELIADES, PhD (@eldemet)
Research Assistant Professor
KIOS Research and Innovation Center of Excellence
University of Cyprus

## Slide 2: Content Contributors
Stelios VRACHIMIS, PhD
Research Associate
(@SteliosVr)
Marios KYRIAKOU
Research Software Engineer (@Mariosmsk)
Pavlos PAVLOU
Research Engineer
(@Ppavlo02)

## Slide 3: Before we begin
Download
  https://github.com/KIOS-Research/ece808-smart-water-systems
Unzip, copy files in your “work” folder (rename!)
Open folder in MATLAB
Run the command “mex –setup”

## Slide 4: KIOS Research and Innovation Center of Excellence
Created in 2008, upgraded to CoE by the EU in 2017
Part of the University of Cyprus (UCY)​, 180+ staff
Strategic collaboration: ​UCY+Imperial College London​
KIOS Innovation Hub -> transitioning local Water Utilities to Smart Water Networks
MSc on Intelligent Critical Infrastructure Systems with ICL/UCY faculty​ (www.msccis.ucy.ac.cy)
Coordinating ERC SyG Water-Futures, H2020 PathoCERT and many others!

## Slide 5: KIOS Smart Water Systems Team
Co-organized the “Battle of Leakage Detection and Isolation Methods” Competition (BATTLEDIM)
Released benchmarks
  L-TOWN EPANET Model
  Leakage Database (leakDB)
Water Security Testbed
KIOS Virtual City & Integrated Platform

## Slide 6: Course structure
Introduction
General Functionality
Research applications
Advanced topics

## Slide 7: EPANET
Created by Lew Rossman
First version in 1993, Second in 2000.
  Now EPA/OWA EPANET v2.2.0 (2020)
Hydraulic and quality simulator for water distribution systems
  Gradient algorithm for hydraulics
  Lagrangian method for computing the PDEs for quality
Simple graphical interface for simulations
Shared library for multiple OS
Salomons, E., Hatchett, S. and Eliades, D.G., 2018, July. The EPANET Open Source Initiative. In WDSA/CCWI Joint Conference Proceedings (Vol. 1).

## Slide 8: The OpenWaterAnalytics (OWA) Community
Open source community supports the development of EPANET since 2015 (kudos to Sam, Elad and Lew)
Established the OWA GitHub repository where EPANET is hosted and updated
  https://github.com/OpenWaterAnalytics/
OWA Forums for Q&A
  http://community.wateranalytics.org
OWA GitHub supports various tools in the EPANET ecosystem
Salomons, E., Hatchett, S. and Eliades, D.G., 2018, July. The EPANET Open Source Initiative. In WDSA/CCWI Joint Conference Proceedings (Vol. 1).

## Slide 9: History of the EPANET-MATLAB Toolkit (EMT)
First version in 2009 as wrapper of EPANET library in MATLAB
Evolved to a MATLAB Class to provide additional capabilities
Development led by KIOS (Marios Kyriakou - @mariosmsk)
Supports EPANET and EPANET-MSX libraries, stand-alone execution
Simple intuitive language & syntax – no need to memorize
Open-source (European Union Public License v.1.2)
Includes a collection of 60+ benchmarks & 20+ examples
Supported through the OWA Forum
Version 2.2.1 includes almost 800 methods, 23K lines of code!
5K downloads in MathWorks
D.G. Eliades, M. Kyriakou, S. Vrachimis and M.M. Polycarpou, "EPANET-MATLAB Toolkit: An Open-Source Software for Interfacing EPANET with MATLAB", in Proc. 14th International Conference on Computing and Control for the Water Industry (CCWI), The Netherlands, Nov 2016, p.8. (doi:10.5281/zenodo.831493)

## Slide 10: New! EPANET-Python Toolkit (EPyT)

## Slide 11: EMT Folder Structure
The EMT Class and libraries
Various Examples in MATLAB
60+ open benchmark networks
Unit-test functions
Load Toolkit

## Slide 12: EMT Class and Libraries
epanet_matlab_toolkit/
  32bit
  64bit
  glnx
  mac
  epanet.m

## Slide 13: The epanet MATLAB Class
MATLAB Classes can “simplify programming tasks that involve specialized data structures or large numbers of functions that interact with special kinds of data.”
The epanet Class is a collection of properties and functions (but not for a specific network)
You can use one Class to create multiple Objects (specific networks)
G includes the Net1 topology and structural values, the simulation parameters, the controls, and all the EMT functions!

## Slide 14: An epanet MATLAB Object
G has
  799 methods (functions)
  363 properties (variables)

## Slide 15: MATLAB and LiveScript
High-level programming environment
Large library of scientific methods (BSD license)
Live Editor for LiveScript (MLX)
Interactive execution of code – great for researchers!
Similar to Jupyter Notebooks for Python
Easy to communicate results & ideas

## Slide 16: Prepare MATLAB for EMT
Windows
  Install App “MinGW-w64 C/C++ Compiler”

## Slide 17: Prepare MATLAB for EMT
Linux
  Use gcc compiler
  Copy “libepanet2.so” to the /lib/ folder (see guide)
macOS
  Use Xcode with Clang compiler
  To avoid security message, allow app “libepanet2.dylib”
  Copy “libepanet2.dylib” to the /usr/local/lib folder

## Slide 18: Quick start with EMT

## Slide 19: Quick start with EMT
Download & unzip
Copy files in your “work” folder (rename!)
Create a new folder “\mywork” and create an empty m or mlx file
Run “start_toolkit” to load toolkit in MATLAB

## Slide 20: General Functionality

## Slide 21: The epanet MATLAB CLass

## Slide 22: Smart Water Networks Research

## Slide 23: Hydraulic state estimation with uncertainty
Vrachimis, S. G.; Timotheou, S.; Eliades, D. G. & Polycarpou, M. M., Iterative Hydraulic Interval State Estimation for Water Distribution Networks, ASCE Journal of Water Resources Planning and Management, vol. 145, p. 04018087, 2018.
Planning - offline
Real-time estimation
Real-time estimation considering uncertainty

## Slide 24: Estimating water quality considering uncertainty
S. G. Vrachimis, D. G. Eliades, and M. M. Polycarpou, “Calculating Chlorine Concentration Bounds in Water Distribution Networks: A Backtracking Uncertainty‐Bounding Approach,” Water Resources Research, p. e2020WR028684, Mar. 2021.
The Backtracking Uncertainty Bounding Approach
Compute bounds of disinfectant concentrations in the network
Incorporates sensor measurements
Considers demand and reaction rate uncertainties
24

## Slide 25: Pressure sensor placement
M. À. Cugueró-Escofet, V. Puig, and J. Quevedo, “Optimal pressure sensor placement and assessment for leak location using a relaxed isolation index: Application to the Barcelona water network,” Control Engineering Practice, vol. 63, pp. 1–12, Jun. 2017.
Challenges
Hundreds of states, only a few sensors
Objectives
Sensitivity of sensors to leakages
Minimize estimation uncertainty
Constraints
Feasible locations
Number of sensors
Detectability, isolability indices
Tools
Pressure sensitivity matrix
S
S

## Slide 26: Leakage simulation and detection
BattLeDIM – Battle of the Leakage Detection and Isolation Methods
  Realistic 2-year simulated SCADA dataset with leakages
  L-TOWN – a benchmark network based on a real city
How to simulate realistic leakages?
How to detect a leakage?
How to localize the leak?
Leakage locations in the Battle of Leakage Detection and Isolation Methods (BATTLEDIM)
S. G. Vrachimis, D. G. Eliades, R. Taormina, Z. Kapelan, A. Ostfeld, S. Liu, M. Kyriakou, P. Pavlou, M. Qiu, and M. M. Polycarpou, “Battle of the Leakage Detection and Isolation Methods,” Journal of Water Resources Planning and Management, (Forthcoming) 2022.

## Slide 27: Water quality sensor placement
Eliades, Demetrios G., and Marios M. Polycarpou. "A fault diagnosis and security framework for water systems." IEEE Transactions on Control Systems Technology 18.6 (2009): 1254-1265.
Multi-objective problem:
  Minimize contamination impact
  Minimize detection delay
Risk-based impact metrics
Challenging problem:
  For 5 water quality sensors 1012 solutions
Best
solutions
Worst
solutions

## Slide 28: Active contamination detection
*Confirm a contamination by driving the contaminant to a sensor
S. G. Vrachimis, R. Lifshitz, D. G. Eliades, M. M. Polycarpou, and A. Ostfeld, “Active Contamination Detection in Water-Distribution Systems,” Journal of Water Resources Planning and Management, vol. 146, no. 4, p. 04020014, Apr. 2020.

## Slide 29: Active contamination detection
Contamination Impact
Number of
valve changes
Pressure
Inputs
Hydraulics
Contamination Impact:
Detection Time:
Constraints:
S. G. Vrachimis, R. Lifshitz, D. G. Eliades, M. M. Polycarpou, and A. Ostfeld, “Active Contamination Detection in Water-Distribution Systems,” Journal of Water Resources Planning and Management, vol. 146, no. 4, p. 04020014, 2020.

## Slide 30: In this tutorial
How to include uncertainties in simulations
How to place pressure sensors
How to create and detect leakage events
How to place quality sensors
How to create and detect contamination events (using MSX)
Network graph theory for contamination analysis

## Slide 31: Advanced topics

## Slide 32: Topics
How to use GitHub
How to create an App
How to publish reproducible research on CodeOcean
How to create an EPANET animation

## Slide 33: Useful links
EPANET Community: https://www.facebook.com/groups/302699687774783
OWA Forum: http://community.wateranalytics.org/